## Slide 1
LeafLens AI Pro
AI-Based Grapevine Disease Detection & Smart Health Monitoring
Niphad Grape Belt, Nashik | Maharashtra, India
Jiya Gavali | Rachi Gedam | Gargi Shinde | Gauri Patil Department of Computer Engineering
PyTorch
MobileNetV3
Raspberry Pi
FastAPI

## Slide 2
Presentation Agenda
01
Viticultural Challenges
Economic impact & disease crisis in Nashik
02
Failure of Current Solutions
Why outdoor vision models don't work for grapes
03
The LeafLens Solution
Chamber + AI + IoT multi-modal fusion
04
System Architecture
End-to-end hardware-software pipeline
05
AI & Explainability
MobileNetV3 + Grad-CAM heatmaps
06
Results & Benchmarks
98.53% accuracy, per-class F1 scores
07
Demo & Future Roadmap
Live demonstration & deployment plan
2/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 3
The Problem: Grapevine Disease Crisis in Nashik
>> Nashik produces over 70% of India's table grape exports; Niphad is the core production hub
>> Downy Mildew (Plasmopara viticola) destroys 40-80% of yield within 5-7 days of humid weather
>> Secondary pathogens: Powdery Mildew & Bacterial Canker cause berry cracking and cane dieback
>> Farmers resort to 15-22 rounds of prophylactic chemical spraying per season (INR 35-50K/acre)
>> Export shipments rejected due to Maximum Residue Limit (MRL) violations
>> Early symptoms visually mimic nutrient deficiency -- naked-eye detection is unreliable
3/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 4
Why Existing Solutions Fail in Viticulture
>> Specular reflection: Grape's waxy cuticle creates harsh glare under outdoor sunlight
>> Generic apps misclassify sunlight glares as white powdery fungal mycelium (false positives)
>> Wind-induced flutter, canopy shadows, and shifting sun angles degrade accuracy
>> Pure CV ignores biology: fungus can't sporulate without specific temperature + humidity
>> PlantVillage-trained models lack regional pathotype and varietal calibration
>> Black-box probability scores fail to convince agronomists -- no spatial evidence
4/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 5
The LeafLens Solution: Multi-Modal Viticulture Platform
>> Portable, light-tight scanning chamber with laboratory-grade standardized illumination
>> CRI 95+ LED ring at 45 degrees eliminates specular reflection from waxy leaves
>> Integrated SHT31 (temp/humidity) + BH1750 (lux) sensors capture microclimate at scan time
>> MobileNetV3-Large: lightweight deep learning backbone (<25 MB, <120ms inference)
>> Grad-CAM heatmaps show exactly WHICH leaf regions triggered the AI diagnosis
>> Multi-modal fusion: visual probability x environmental risk multiplier
>> ICAR-NRCG aligned spray advisories with exact chemical formulations
5/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 6
End-to-End System Architecture
Grape Leaf Sample
-->
Scanning Chamber (Rachi)
-->
FastAPI Backend (Gargi)
-->
AI Engine MobileNetV3 (Jiya)
-->
Grad-CAM + Risk Fusion
-->
Farmer Dashboard (Gauri)
Camera: Pi Camera Module 3 (Sony IMX708) | Sensors: SHT31 + BH1750 (I2C)
API: POST /api/v1/scan | Database: SQLite persistent audit trail
UI: Streamlit with live camera, Grad-CAM viewer, 30-day trends, English/Marathi
6/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 7
Hardware Innovation: Standardized Scanning Chamber
>> Enclosure: 20x20x25 cm matte-black acrylic, light-absorbing flocking interior
>> Camera: Raspberry Pi Camera Module 3 (12MP Sony IMX708, autofocus, HDR)
>> Lighting: 5500K CRI 95+ LED ring at 45-degree angle with diffuser -- zero glare
>> Temperature + Humidity: Sensirion SHT31-D (+/- 0.2C, +/- 1.5% RH) via I2C at 0x44
>> Light Sensor: BH1750 16-bit illuminance sensor (I2C at 0x23) verifies chamber seal
>> One-touch scan: GPIO 17 push-button with dual-color LED status (GPIO 27)
>> Total BOM cost: INR 8,250 to 10,250 (commercial off-the-shelf components)
7/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 8
AI Model: MobileNetV3-Large Transfer Learning
>> Backbone: MobileNetV3-Large pre-trained on ImageNet-1K (hard-swish, SE attention)
>> 4 Disease Classes: Downy Mildew | Powdery Mildew | Bacterial Leaf Spot | Healthy
>> Dataset: 2,726 authentic Niphad grape leaf images (70/15/15 train/val/test split)
>> Augmentations: Random flip (H:0.5, V:0.3), rotation (+/-25 deg), color jitter
>> Optimizer: AdamW (lr=0.0003, weight_decay=1e-4) with CosineAnnealing scheduler
>> Training: 15 epochs --> Best validation accuracy: 98.53% at epoch 3
>> Model size: <25 MB | Inference: <120ms on CPU
8/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 9
Explainability: Grad-CAM Visual Attention Heatmaps
>> Problem: Farmers won't trust a black-box probability number without visual proof
>> Grad-CAM targets final conv layer of MobileNetV3 feature extractor
>> Computes gradient of predicted class score w.r.t. feature activation maps
>> ReLU-filtered weighted sum produces coarse attention heatmap (Jet colormap overlay)
>> Downy Mildew: attention focuses on angular chlorotic oil spots & veinal necrosis
>> Powdery Mildew: highlights white powdery mycelial patches across leaf lamina
>> HSV color thresholding quantifies exact % of necrotic tissue area
9/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 10
Multi-Modal Fusion: Microclimate Risk Integration
>> Vapor Pressure Deficit (VPD): VP_sat = 0.61078 * exp(17.27*T / (T+237.3))
>> VPD = VP_sat * (1 - RH/100) | VPD < 0.50 kPa = ideal for fungal sporulation
>> Downy Mildew risk: 18-26C + RH>80% + leaf wetness = CRITICAL ALERT
>> Powdery Mildew risk: 20-32C + RH 45-70% = ELEVATED ALERT
>> Multi-Modal Risk Multiplier fuses visual P_CV with environmental R_env
>> Health Score = 100 - (P_fused * 65 * S_k + NecrosisRatio * 0.35 + VPD_penalty)
>> Score 0-40: CRITICAL | 40-70: ELEVATED | 70-100: LOW RISK
10/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 11
Backend: FastAPI REST API & Recommendation Engine
>> FastAPI async gateway with auto-generated Swagger docs at /docs
>> POST /api/v1/scan: image + sensor JSON --> full diagnostic JSON (<450ms)
>> GET /api/v1/history: chronological scan records for vineyard health tracking
>> GET /api/v1/analytics: aggregate disease distribution & health indices
>> SQLite (leaflens.db): persistent audit trail with 16-column scan records
>> ICAR-NRCG spray prescriptions:
- Downy: Metalaxyl 8% + Mancozeb 64% WP @ 2.5 g/L + canopy de-suckering
- Powdery: Wettable Sulfur 80% WDG @ 2.0 g/L + canopy aeration
- Bacterial: Copper Oxychloride 50% WP @ 2.5 g/L + Streptocycline 0.1 g/L
11/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 12
Farmer Dashboard: Interactive Bilingual Interface
>> Built with Streamlit -- responsive for tablets, laptops, field kiosks
>> 3 input modes: Live camera capture | Image upload | Pre-loaded Niphad test library
>> Side-by-side viewer: Original leaf photo + AI Grad-CAM lesion heatmap
>> Real-time Health Score gauge (0-100) with color-coded risk alerts
>> Microclimate dashboard: Temperature, Humidity, VPD, Leaf Wetness status
>> 30-day vineyard epidemiological trend charts (Plotly)
>> Full Marathi localization toggle for Nashik farmers
12/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 13
Results: Training Metrics & Benchmark Performance
Epoch
Train Loss
Train Acc
Val Loss
Val Acc
1
0.2873
89.88%
0.2996
92.63%
2
0.0738
97.59%
0.2915
93.86%
3
0.0384
98.53%
0.0648
98.53%
4
0.0444
98.85%
0.0910
97.30%
5
0.0118
99.53%
0.0839
98.03%
Best Validation Accuracy: 98.53%
Macro-Averaged F1-Score: 0.985
Downy Mildew: P=98.8% R=98.5% F1=0.986
Powdery Mildew: P=98.1% R=98.3% F1=0.982
Bacterial Spot: P=97.9% R=98.2% F1=0.980
Healthy Foliage: P=99.2% R=99.1% F1=0.991
13/15
LeafLens AI Pro | Grapevine Disease Detection

## Slide 14
Live Demonstration Protocol
Step 1
Open dashboard at http://localhost:8501 and verify backend at port 8000
Step 2
Select Downy Mildew sample from Niphad test library (or use live camera)
Step 3
Observe real-time classification: Downy Mildew with 100% confidence
Step 4
Review side-by-side Grad-CAM heatmap highlighting lesion regions
Step 5
Adjust humidity slider >80% + enable leaf dew --> watch CRITICAL ALERT trigger
Step 6
Toggle language to Marathi to see localized disease names & spray advisories
14/15

## Slide 15
Future Roadmap & Conclusion
>> ONNX INT8 quantization for offline inference on Raspberry Pi Zero 2W (<INR 1,500)
>> Autonomous vineyard rovers & multispectral drone payload for row-level scouting
>> Expand disease coverage: Anthracnose, Esca, Iron/Boron/Magnesium deficiencies
>> Field trials with Sahyadri Farms FPO (Mohadi, Nashik) & ICAR-NRCG (Manjri, Pune)
>> Projected impact: 30-40% reduction in prophylactic fungicide spraying
>> Protect export consignments from MRL rejections, preserve farmer income
Thank You!
Jiya Gavali | Rachi Gedam | Gargi Shinde | Gauri Patil
We welcome your questions and feedback.
15/15